## Slide 1
B.Sc. THESIS DEFENSE
An Ultra-Low-Power 10-Transistor
1-Bit Magnitude Comparator
Using Gate Diffusion Input (GDI) Technique
Transistor-Level VLSI Circuit Optimization Across 180nm, 90nm & 45nm PTM Nodes
PRESENTER
Shahrear Hossain
Matric No: ET223104
Dept. of Electrical & Electronic Engineering
International Islamic University Chittagong
SUPERVISOR
Riazul Islam
Lecturer, Dept. of EEE, IIUC
October 2026

## Slide 2
DEPARTMENT OF EEE, IIUC | B.Sc. THESIS DEFENSE
Presentation Roadmap & Agenda
Shahrear Hossain (ID: ET223104) | 10T GDI 1-Bit Magnitude Comparator
01
Introduction
VLSI scaling, low-power constraints & motivation.
02
Problem Statement
Limitations of 26T CMOS & 16T Transmission Gate designs.
03
Proposed Solution
10-Transistor GDI magnitude comparator architecture.
04
Methodology
LTSpice simulation setup across 180nm, 90nm & 45nm PTM.
05
Results & Discussion
Transient output waveforms, power, delay & PDP analysis.
06
Conclusion
Summary of contributions & future multi-bit ALU scope.

## Slide 3
DEPARTMENT OF EEE, IIUC | B.Sc. THESIS DEFENSE
1. Introduction & Research Background
Shahrear Hossain (ID: ET223104) | 10T GDI 1-Bit Magnitude Comparator
VLSI Technology Scaling Challenges
• Exponential Device Scaling: Deep sub-micron nodes face high static leakage & dynamic power. • Battery & Thermal Constraints: Portable IoT & biomedical CPUs require sub-microwatt operation. • Essential Arithmetic Block: Magnitude comparators govern speed in ALUs, DSPs & ADCs.
Power Density & Integration Trend

## Slide 4
DEPARTMENT OF EEE, IIUC | B.Sc. THESIS DEFENSE
2. Problem Statement: Conventional Comparator Limitations
Shahrear Hossain (ID: ET223104) | 10T GDI 1-Bit Magnitude Comparator
Static CMOS (26T)
• Heavy 26-transistor count.
• Large silicon layout footprint.
• High internal parasitic capacitance.
Transmission Gate (16T)
• Requires 16 transistors.
• Dual inverted control lines (A, A').
• High interconnect routing overhead.
Pass Transistor (12T)
• 12 to 14 transistor budget.
• Severe Vth threshold voltage drop.
• Signal degradation at low VDD.

## Slide 5
DEPARTMENT OF EEE, IIUC | B.Sc. THESIS DEFENSE
3. Proposed Solution: 10T GDI Magnitude Comparator
Shahrear Hossain (ID: ET223104) | 10T GDI 1-Bit Magnitude Comparator
Proposed Circuit Innovations
• 61.5% Transistor Reduction: Cut total count from 26T down to only 10 Transistors. • Gate Diffusion Input (GDI): Uses 2-transistor primitive cells to execute complex logic. • Zero Hardware Redundancy: Directly computes A<B, A>B, and A=B without extra buffers.
10T GDI Circuit Schematic Diagram

## Slide 6
DEPARTMENT OF EEE, IIUC | B.Sc. THESIS DEFENSE
4. Methodology & Simulation Framework
Shahrear Hossain (ID: ET223104) | 10T GDI 1-Bit Magnitude Comparator
LTSpice XVII Simulation Setup
• Technology Models: Predictive Technology Model (PTM) 180nm, 90nm & 45nm. • Supply Voltage Scaling: 1.8V (180nm), 1.2V (90nm), and 0.8V - 1.0V (45nm). • Input Test Vectors: Transient pulses at 100 MHz to 1 GHz frequencies.
Implementation Scope & Verification
SOFTWARE SIMULATION STUDY
• Validation is strictly simulation-based (SPICE level).
• No physical IC fabrication / hardware tape-out.
• Measured Metrics: 1. Average Power Dissipation (Pavg) 2. Propagation Delay (tpd at 50% transition) 3. Power-Delay Product (PDP = Pavg × tpd)

## Slide 7
DEPARTMENT OF EEE, IIUC | B.Sc. THESIS DEFENSE
4. Gate Diffusion Input (GDI) Cell Mechanics
Shahrear Hossain (ID: ET223104) | 10T GDI 1-Bit Magnitude Comparator
2-Transistor GDI Cell
GDI Cell inputs (P, N, G) accept arbitrary logic variables, enabling complex functions in just 2 transistors.
Comparator Output Equations
1. A < B Output (GDI Cell 1 - 2T): Equation: A < B = A' · B 2. A > B Output (GDI Cell 2 - 2T): Equation: A > B = A · B' 3. A = B Output (NOR / XNOR Stage - 6T): Equation: A = B = ((A < B) + (A > B))' = A ⊙ B Total Budget: 2T + 2T + 6T = 10 Transistors

## Slide 8
DEPARTMENT OF EEE, IIUC | B.Sc. THESIS DEFENSE
5. Results: Quantitative Performance Comparison (45nm)
Shahrear Hossain (ID: ET223104) | 10T GDI 1-Bit Magnitude Comparator
Performance Comparison Table at 45nm PTM Node (VDD = 1.0V)
Architecture Style | Transistor Count | Delay (tpd) [ps] | Power (Pavg) [µW] | PDP [aJ]
Static CMOS | 26T | 48.2 ps | 14.82 µW | 714.3 aJ
Transmission Gate (TG) | 16T | 31.5 ps | 8.94 µW | 281.6 aJ
Pass Transistor (PTL) | 12T | 27.8 ps | 6.45 µW | 179.3 aJ
Proposed GDI Design | 10T (-61.5%) | 18.4 ps (-61.8%) | 2.15 µW (-85.4%) | 39.56 aJ (18× Better)
Key Takeaway: The proposed 10T GDI comparator achieves 85.4% lower power and 18× lower PDP compared to standard 26T CMOS.

## Slide 9
DEPARTMENT OF EEE, IIUC | B.Sc. THESIS DEFENSE
5. Results: Graphical Comparison Across Topologies
Shahrear Hossain (ID: ET223104) | 10T GDI 1-Bit Magnitude Comparator
Propagation Delay (ps)
Average Power (µW)
Power-Delay Product (aJ)

## Slide 10
DEPARTMENT OF EEE, IIUC | B.Sc. THESIS DEFENSE
5. Performance Analysis & Design Trade-offs
Shahrear Hossain (ID: ET223104) | 10T GDI 1-Bit Magnitude Comparator
85.4%
POWER REDUCTION
Eliminates redundant switching paths and reduces internal node capacitance drastically.
61.5%
AREA SAVINGS
Transistor count cut from 26T to 10T, freeing up valuable silicon real estate.
18×
PDP IMPROVEMENT
Power-Delay Product drops to 39.56 aJ, representing state-of-the-art energy efficiency.

## Slide 11
DEPARTMENT OF EEE, IIUC | B.Sc. THESIS DEFENSE
6. Conclusion & Future Scope
Shahrear Hossain (ID: ET223104) | 10T GDI 1-Bit Magnitude Comparator
Summary of Key Contributions
• Successful 10T GDI Implementation: Demonstrated ultra-low-power 1-bit comparator using only 10 transistors. • Excellent Submicron Scalability: Maintained superior performance across 180nm, 90nm & 45nm PTM nodes. • Benchmark Energy Efficiency: Achieved 2.15 µW power and 18.4 ps delay at 45nm node.
Future Research Scope
• Multi-Bit ALU Integration: Extend 1-bit cell to 4-bit, 8-bit & 64-bit high-speed comparators. • Buffer Restoration Stages: Integrate swing restoration buffers for deep cascade architectures. • Layout & PVT Corner Analysis: Perform Monte-Carlo Process, Voltage & Temperature variations.

## Slide 12
Thank You!
Questions & Answers
PRESENTER CONTACT INFORMATION
Shahrear Hossain
Matric No: ET223104
Department of Electrical and Electronic Engineering
International Islamic University Chittagong (IIUC)