## Slide 1: AN ULTRA LOW POWER 10 TRANSISTOR 1 BIT MAGNITUDE COMPARATOR USING GATE DIFFUSION INPUT TECHNIQUE
Supervised by:
Riazul Islam
Lecturer
Shahrear Hossain Shawon
ID: ET223104
Department of
Electrical and Electronic Engineering
INTERNATIONAL ISLAMIC UNIVERSITY CHITTAGONG

## Slide 2: INTRODUCTION
PROBLEM STATEMENT
OBJECTIVES
METHODOLOGY
LITERATURE REVIEW
INTRODUCTION TO COMPARATOR
CMOS LOGIC STYLES
CIRCUIT DESIGN COMPARE IN VARIOUS TECHNIQUE
Table of Contents
01

## Slide 3
Table of Contents
SIMULATION & RESULTS
PERFORMANCE COMPARISON
CONCLUSION
FUTURE WORK
02

## Slide 4: INTRODUCTION
Magnitude comparators are fundamental building blocks in digital VLSI systems, used to compare two binary inputs and determine A greater than B, A less than B, or A equal to B.
They play a crucial role in arithmetic logic units (ALUs), processors, memory address decoding, digital controllers, and embedded systems.
The growing demand for ultra-low-power and high-speed integrated circuits has increased the need for comparator designs with lower transistor count, reduced power consumption, and faster propagation delay
This thesis proposes and analyzes an Ultra-Low-Power 10-Transistor 1-Bit Magnitude Comparator using the Gate Diffusion Input (GDI) Technique, and evaluates its performance in terms of power, propagation delay, and power-delay product (PDP) across 180 nm, 90 nm, and 45 nm PTM technology nodes.
.
03

## Slide 5: PROBLEM STATEMENT
High transistor count in conventional CMOS comparators.
Increased power consumption and silicon area.
Higher propagation delay due to complex logic paths.
Leakage current and parasitic capacitance at scaled technology nodes.
Need for an ultra-low-power, high-speed comparator design.
GDI technique offers reduced transistor count and improved efficiency.
Comparative evaluation is required using Power, Delay, PDP, and Transistor Count.
04

## Slide 6: OBJECTIVES
01
To design and simulate 1 Bit Comparator using CMOS GDI technique.
02
Reduce Transistor Number of the Comparator
03
To evaluate and compare key performance parameters such as:
Rise time, Fall time, Propagation delay, Power consumption. PDP
05

## Slide 7: METHODOLOGY
06

## Slide 8: LITERATURE REVIEW
Researcher | Year | Contribution | Drawback
Arvind Kumar, Manoj Kumar | 2017 | Proposed a 1-bit CMOS comparator using transistor stacking across its XNOR and AND gates to reduce active-mode leakage power | Marginally higher propagation delay () and increased transistor count due to splitting transistors into series pairs.
Dheeraj Tailor, Tavesh Sharma, Manoj Mumar | 2019 | Designed a 1-bit CMOS comparator utilizing MTCMOS (for NOR gates) and Forced Stacking (for inverters) to minimize subthreshold leakage and active power. | MTCMOS is a state-destructive technique (outputs from active mode are lost in standby mode); requires additional sleep control signal routing.
Samiha Lubaba, K. M. Faisal , Moumita Sadia Islam, Mehedi Hasan. | 2020 | Developed a 2-bit hybrid magnitude comparator using PTL/TGL-based XNOR gates for low-latency internal signal generation combined with C-CMOS output logic for high driving power and full swing. | Requires a total of 46 transistors; average power dissipation (7.792 µW) remains slightly higher than pure GDI-based architectures.
Yashmit Sharma, Premananda B.S, Divyanshu Ra, Kshitij Pandey | 2025 | Created a 1-bit hybrid comparator combining a 6T-MUX PTL Full Adder with TGL output gates, achieving a 22-transistor footprint and power reduction | Pass-transistor pathways can exhibit threshold voltage drop unless carefully sized/driven; requires inverted input signals ().
Researcher | Year | Contribution | Drawback
Arvind Kumar, Manoj Kumar | 2017 | Proposed a 1-bit CMOS comparator using transistor stacking across its XNOR and AND gates to reduce active-mode leakage power | 
Dheeraj Tailor, Tavesh Sharma, Manoj Mumar | 2019 | Designed a 1-bit CMOS comparator utilizing MTCMOS (for NOR gates) and Forced Stacking (for inverters) to minimize subthreshold leakage and active power. | MTCMOS is a state-destructive technique (outputs from active mode are lost in standby mode); requires additional sleep control signal routing.
Samiha Lubaba, K. M. Faisal , Moumita Sadia Islam, Mehedi Hasan. | 2020 | Developed a 2-bit hybrid magnitude comparator using PTL/TGL-based XNOR gates for low-latency internal signal generation combined with C-CMOS output logic for high driving power and full swing. | Requires a total of 46 transistors; average power dissipation (7.792 µW) remains slightly higher than pure GDI-based architectures.
Yashmit Sharma, Premananda B.S, Divyanshu Ra, Kshitij Pandey | 2025 |  | 
07

## Slide 9: INTRODUCTION TO Comparator
Definition: A digital magnitude comparator is a combinational logic circuit used to compare two binary numbers ( and ) and determine their relative numerical values.
Output Signals: It generates three distinct output signals to indicate the exact comparison result: (Greater Than), (Less Than), and (Equal To).
Implementation Techniques: Designed using various CMOS logic styles such as Complementary CMOS (C-CMOS), Transmission Gate Logic (TGL), Pass Transistor Logic (PTL), and Gate Diffusion Input (GDI).
Applications: Used in ALU, processors, memory circuits, address decoding, and digital control systems.
09

## Slide 10: CMOS Logic Styles
10
Logic Style | Key Features & Characteristics
Static Logic | Uses pMOS and nMOS in complementary fashion Stable output maintained without clock Low power dissipation when idle
PTL Logic | Passes signals directly through single MOS switches to save area Uses fewer transistors, lowering overall dynamic power usage Loses voltage level (Vth drop) when passing a logic 1
TG Logic | Connects NMOS and PMOS in parallel to pass full logic levels Prevents voltage drop, giving clean strong 0 and 1 outputs Needs inverted control signals, which increases routing complexity
GDI Logic | Uses a 3-input cell to implement complex functions in few transistors Cuts down power and area for circuits like XOR and MUX Needs special twin-well CMOS fabrication to avoid body effect issues.

## Slide 11: CIRCUIT DESIGN COMPARE IN VARIOUS TECHNIQUE
Static CMOS (32T)
Fig 01: Static CMOS
11
Input A | Input B | A > B | A = B | A < B
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0
Fig 02: Truth table

## Slide 12: CIRCUIT DESIGN COMPARE IN VARIOUS TECHNIQUE
Transmission Gate (16T)
Fig 03: TG CMOS
11
Input A | Input B | A > B | A = B | A < B
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0
Fig 04: Truth table

## Slide 13: CIRCUIT DESIGN COMPARE IN VARIOUS TECHNIQUE
Pass Transistor (10T)
Fig 05: PTL CMOS
11
Input A | Input B | A > B | A = B | A < B
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0
Fig 06: Truth table

## Slide 14: CIRCUIT DESIGN COMPARE IN VARIOUS TECHNIQUE
Proposed 10 Transistor
Fig 07: Proposed GDI CMOS
11
Input A | Input B | A > B | A = B | A < B
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0
Fig 08: Truth table

## Slide 15: SIMULATION & RESULTS
Fig 09 : Output Waveshape
15

## Slide 16: SIMULATION & RESULTS
15
Design / Reference Paper | Propagation Delay | Average Power Dissipation | PDP (Power-Delay Product)
Static CMOS Paper (2017) | 49.38 ns | 174.352 pW | 0.0086 fJ
MTCMOS Paper (2019) | 330.61 ps | 48.12 pW | 0.0000159 fJ
Static, Pass, TG Paper (2020) | 0.192 ns | 7.792 µW | 1.496 fJ
6T MUX Adder Comparator (2025) | 5.5 ps | 7.3 µW | 0.04 fJ
My Proposed Design | 336 ps | 34.18 pW | 0.0000114 fJ

## Slide 17: PERFORMANCE COMPARISON
Propagation Delay Bar Chart
Average Power Dissipation Bar Chart
PDP (Energy per Operation) Bar Chart
Fig 10 : Propagation Delay
Fig 11 : Average Power Dissipation
Fig 12: Product Delay Propagation
16

## Slide 18: KEY FINDINGS
GDI Technique demonstrate:
Its low power consumption.
Provides short propagation delay.
Requires fewer transistors.
CMOS still viable for cost-sensitive applications
17

## Slide 19: CONCLUSION
CMOS faces scalability and performance limitations
GDI technique addresses these with superior design
For future VLSI design, GDI technique offers better performance and efficiency
LTspice simulations confirm performance gains in GDI based designs
18

## Slide 20: Future Work
Study GDI Technique under varied temperatures and voltages
Analyze integration into larger digital blocks (e.g., ALUs)
Explore hybrid logic families for ultra-low power designs
Investigate real-time implementations using FPGA or ASIC platforms
Evaluate GDI performance in logic-intensive circuits like full adders or multiplexers
Explore noise immunity and signal integrity analysis in GDI Technique
Extend simulations to beyond to analyze scalability
19

## Slide 21: REFERENCES
[1] A. Kumar and M. Kumar, “Improved Design of CMOS 1-Bit Comparator with Stacking Technique,” International Journal of Current Engineering and Technology, Vol. 7, no. 3, pp. 1044–1047, 2017.
[2] D. Tailor, T. Sharma, and M. Kumar, “Design of CMOS Based 1-bit Comparator with MTCMOS and Forced Stack Technique in 180µm Technology,” in Proc. 2019 IEEE International Conference on Signal Processing and Communication (ICSC), NOIDA, India, pp. 330–334, 2019.
[3] S. Lubaba, M. S. Islam, K. M. Faisal, and M. Hasan, “Design of a Two-Bit Magnitude Comparator Based on Pass Transistor, Transmission Gate and Conventional Static CMOS Logic,” in Proc. 2020 IEEE Region 10 Symposium (TENSYMP), Dhaka, Bangladesh, pp. 1114–1117, 2020.
[4] Y. Sharma, B. S. Premananda, D. Raj, and K. Pandey, “Design and Analysis of a 1-bit Comparator for Low Power VLSI Systems,” in Proc. 2025 Third International Conference on Networks, Multimedia and Information Technology (NMITCON), Bengaluru, India, pp. 1–6, 2025.
20

## Slide 22: THANK
YOU