## Slide 1
Logic Style | Key Features & Characteristics
Static Logic | Uses pMOS and nMOS in complementary fashion Stable output maintained without clock Low power dissipation when idle
PTL Logic | Passes signals directly through single MOS switches to save area Uses fewer transistors, lowering overall dynamic power usage Loses voltage level (Vth drop) when passing a logic 1
TG Logic | Connects NMOS and PMOS in parallel to pass full logic levels Prevents voltage drop, giving clean strong 0 and 1 outputs Needs inverted control signals, which increases routing complexity
GDI Logic | Uses a 3-input cell to implement complex functions in few transistors Cuts down power and area for circuits like XOR and MUX Needs special twin-well CMOS fabrication to avoid body effect issues
Logic Styles Comparison Table